## Slide 1
Name:
Specification and learning objectives
By the end of this topic, you will have studied:
Simple logic diagrams using the operators AND, OR and NOT.
Truth tables.
Combining Boolean operators (AND, OR and NOT) to two levels.
Applying logical operators in truth tables to solve problems.
Resources
We recommend the OCR-endorsed textbook from PG Online for use during your GCSE studies.
Craig ‘n’ Dave videos for SLR 2.4
Notes: Activity…

## Slide 2: Simple logic diagrams using the operators AND, OR and NOT
Logic gates are the fundamental building blocks of digital integrated circuits. They are what a computer CPU and arithmetic logic unit are made of. Logic gates can be drawn with an image representing the gate or written with a character.
A | B | Output
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | B | Output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | Output
0 | 1
1 | 0
A
B
A
B
A
Notes: In the box underneath each symbol, label the three logic gates: NOT, AND, OR
In the second box underneath, input the symbol for each gate: ∨ ¬ ∧
Complete the truth tables for each logic gate. Use these logic gate symbols to complete the exercises on the following slides.

## Slide 3: Combining Boolean operators (AND, OR and NOT) to two levels
Logic diagram for the expression: A AND C
Alternative notation: A ∧ C
Notes: Draw the logic gate for the expression: A AND C

## Slide 4: Combining Boolean operators (AND, OR and NOT) to two levels
Logic diagram for the expression: (A OR B) AND C
Alternative notation: (A V B) ∧ C
Notes: Draw the logic gate for the expression: (A OR B) AND C

## Slide 5: Combining Boolean operators (AND, OR and NOT) to two levels
Logic diagram for the expression: (NOT A) OR B
Alternative notation: ¬A V B
Notes: Draw the logic gate for the expression: NOT A OR B

## Slide 6: Combining Boolean operators (AND, OR and NOT) to two levels
Logic diagram for the expression: (A AND B) OR (C AND D)
Alternative notation: (A ∧ B) V (C ∧ D)
Notes: Draw the logic gate for the expression: (A AND B) OR (C AND D)

## Slide 7: Combining Boolean operators (AND, OR and NOT) to two levels
Logic diagram for the expression: NOT(A AND B)
Alternative notation: ¬(A ∧ B)
Notes: Draw the logic gate for the expression: NOT (A AND B)

## Slide 8: Applying logical operators in truth tables to solve problems
A
B
C
D
A | B | C | D
0 | 0 | 0 | 1
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
A
B
C
D
A | B | C | D
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
Notes: Complete the truth table for the expression: NOT (A AND B)
Complete the truth table for the expression: NOT (A OR B)

## Slide 9: Applying logical operators in truth tables to solve problems
A
B
C
A | B | C | D | E | F
0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 0 | 0
F
D
E
Notes: Complete the truth table for the expression: (A AND B) AND NOT C

## Slide 10: Applying logical operators in truth tables to solve problems
A
B
C
A | B | C | D | E | F
0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 0 | 1
F
D
E
Notes: Complete the truth table for the expression: (A OR B) OR NOT C

## Slide 11: Applying logical operators in truth tables to solve problems
A
B
C
A | B | C | D | E | F
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 1 | 0
F
D
E
Notes: Complete the truth table for the expression: NOT A AND (B OR C)

## Slide 12: Applying logical operators in truth tables to solve problems
A
C
D
A | B | C | D | E | F | G
0 | 0 | 0 | 0 |  |  | 
0 | 0 | 0 | 1 |  |  | 
0 | 0 | 1 | 0 |  |  | 
0 | 0 | 1 | 1 |  |  | 
0 | 1 | 0 | 0 |  |  | 
0 | 1 | 0 | 1 |  |  | 
0 | 1 | 1 | 0 |  |  | 
0 | 1 | 1 | 1 |  |  | 
1 | 0 | 0 | 0 |  |  | 
1 | 0 | 0 | 1 |  |  | 
1 | 0 | 1 | 0 |  |  | 
1 | 0 | 1 | 1 |  |  | 
1 | 1 | 0 | 0 |  |  | 
1 | 1 | 0 | 1 |  |  | 
1 | 1 | 1 | 0 |  |  | 
1 | 1 | 1 | 1 |  |  | 
G
E
F
B
Notes: Complete the truth table for the expression: (A OR B) AND (C OR D)

## Slide 13: Applying logical operators in truth tables to solve problems
A
C
D
A | B | C | D | E | F | G
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 0 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 1 | 1 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0
1 | 1 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1
G
E
F
B
Notes: Complete the truth table for the expression: (A OR B) AND (C AND D)

## Slide 14: Applying logical operators in truth tables to solve problems
A
C
D
A | B | C | D | E | F | G
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 0 | 1 | 1
1 | 1 | 0 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 0 | 1
1 | 1 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
G
E
F
B
Notes: Complete the truth table for the expression: (A AND B) OR (C AND D)

## Slide 15: Create, complete or edit logic diagrams and truth tables for given scenarios
A | B | C | W = A AND B | X = W OR C
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1
Scenario: “An alarm goes off (OUTPUT X) if a movement sensor is triggered (INPUT A) AND it is also night (INPUT B). Regardless of these prerequisites, the alarm should always go off if someone triggers the alarm manually (INPUT C).”
Notes: Read the scenario presented on the slide
In the box, complete the logic diagram for this scenario – you can use the logic gate symbols from the other slides.
Complete the truth table for the logic diagram – you made use the intermediate outputs as well.

## Slide 16: Create, complete or edit logic diagrams and truth tables for given scenarios
A | B | C | D | V = A OR B | W = C OR D | X = V AND W
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 1 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
Scenario: “A holding cell in a police station has two electronic security doors (INPUT A and INPUT B). If the camera is on (INPUT C) OR the occupied sign is on (INPUT D) AND either of the doors has not properly been closed, a warning speaker should sound (OUTPUT X).”
Notes: Read the scenario presented on the slide
In the box, complete the logic diagram for this scenario – you can use the logic gate symbols from the other slides.
Complete the truth table for the logic diagram – you made use the intermediate outputs as well.

## Slide 17: Create, complete or edit logic diagrams and truth tables for given scenarios
A | B | C | V = A OR B | W = NOT C | X = V AND W
0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 0 | 0
1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 0 | 0
Scenario: “A factory has an automated manufacturing system that operates in an ON state (OUTPUT X) if it is either switched on by an operator (INPUT A) OR a computer triggers a scheduled production run (INPUT B). The system also has an emergency override (INPUT C) that, in its normal operating state, is feeding no signal to the computer system, However, when it is pressed, it triggers a positive TRUE state (1), which should result in the system shutting down.”
Notes: Read the scenario presented on the slide
In the box, complete the logic diagram for this scenario – you can use the logic gate symbols from the other slides.
Complete the truth table for the logic diagram – you made use the intermediate outputs as well.

## Slide 18
Assessment |  |  |  | Target: |  | Overall grade:
Minimum expectations by the end of this unit |  |  |  |  |  | 
 | Learn terms 218-223 from GCSE Level Key Terminology. |  |  |  |  | 
 | Complete all pages of the workbook. |  |  |  |  | 
 | Score 80% in the end-of-unit test. |  |  |  |  | 
Feedback |  |  |  |  |  | 
Breadth |  | Depth |  |  | Understanding | 
 All aspects complete |  |  Excellent level of depth |  |  |  All work is accurate | 
 Most aspects complete |  |  Good level of depth |  |  |  Most work is accurate | 
 Some aspects complete |  |  Basic level of depth shown |  |  |  Some work is accurate | 
 Little work complete |  |  Little depth and detail provided |  |  |  Little work is accurate | 
Comment and action |  |  | Student response |  |  | 

## Slide 19
Reflection and Revision checklist | 
Confidence | Clarification
   | I can construct simple logic diagrams using the operators AND, OR and NOT.
   | I can construct truth tables for the operators AND, OR and NOT.
   | I can construct a truth table for a given logic diagram.
   | I can apply logical operators in appropriate truth tables to solve problems.
My revision focus: |